Instructions for writing IMEI number tool

Install the driver first, see the video for the operation

Only supports WIN7 system

I. Software use

1. Open the folder SN_Write_tool_exe_v2.1448.00, and run SN Writer.exe;

2. Settings, as shown below,

3. Set system config, click the button, and check the options as shown below:

Click ‘MD_DB’, select the ‘Database’ file beginning with ‘BPLG...’ in the software package according to the path, and click ‘save’ to save it.

4. Click ‘Start’, enter or scan the required ‘IMEI’ number, and click ‘OK’

5. Insert the motherboard ‘usb’ in the shutdown state into the computer and wait for about 5 seconds, the following picture will appear

If ‘PASS’ appears, it means the burning is successful; continue to enter the next imei number, click OK to insert the next motherboard, and then proceed to batch imei burning in sequence.